## Slide 1
RESEARCH TRACK II · COGAR ASSIGNMENT C2b
Does Fusing Deformation and Shear Improve Tactile Material Classification?
An ablation study under contact-condition variability
Amr Magdy Mohamed Elsayed Abdalla
S8082888
DIBRIS, University of Genoa · PROFESSOR MASTROGIOVANNI FULVIO , G. Galvagni

## Slide 2
INTRODUCTION
Why touch — and the research question
Vision fails on look-alikes. Two objects can look identical yet differ in stiffness, texture, or compliance. Touch reveals the mechanical response of a contact, independent of appearance.
A vision-based tactile sensor exposes two physical channels:
Deformation
normal/vertical displacement → contact geometry
Shear
lateral/tangential displacement → tangential force
RESEARCH QUESTION (PICO)
Does fusing deformation + shear improve classification accuracy on everyday objects, compared to either modality alone — and how robustly as contact conditions vary?
H1 fusion > best single modality
H2 advantage persists as variability grows
H3 each modality fails on a predictable subset
2

## Slide 3
LITERATURE ANALYSIS
Four works — from sensing principles to SOTA
1
GelSight (2017)
FOUNDATION
Elastomer deformation = geometry; marker motion ∝ force. Grounds our two channels.
2
Amin et al. (2023)
LAB / PIPELINE PRECEDENT
Same lab & Baxter; SVM/SLFNN/CNN on hardness. But PVDF pressure, and mean/std features.
3
Liao et al. (2025)
SENSOR REFERENCE
Daimon DM-Tac; hardness from normal-force dynamics — decomposes shear but discards it.
4
FG-CLTP (2025)
SOTA CEILING
Contrastive language–tactile pretraining; quantitative contact states beat texture labels (95.9%).
Our position: the only study using deformation+shear as a fused modality, with the controlled single-vs-fused ablation none of the four perform.
3

## Slide 4
METHODOLOGICAL PROPOSAL
Sensor, data, and an honest pipeline
Sensor
Daimon WS vision-based tactile sensor. Per frame: deformation + shear fields → (T, 30×40, 4).
Dataset
10 materials (rigid, compliant, textured) × 2 contact modes × 20 trials. Hand-collected, release-gated.
Models
Classical: SVM / RF / XGBoost on 30 features. Deep: CNN → BiLSTM → temporal self-attention.
Honest eval
5-fold CV; early stopping on an internal validation split — the test fold is never used for selection.
Two contact modes are the variability axis: press (controlled) vs airhold (variable, stronger shear).
4

## Slide 5
EXPERIMENT DESIGN
One constraint shaped the whole study
THE CONSTRAINT
Robot access was limited, so data were hand-collected. Applied force is therefore not constant — it is partially confounded with material identity.
→ Results are validation-grade, not force-controlled-deployment-grade. We state this first, not last.
TURNED INTO AN ADVANTAGE
The two contact modes directly probe robustness to this variability:
press — a controlled, consistent contact
airhold — squeezed in the air: more variable, stronger shear
Comparing them tests H2 head-on.
5

## Slide 6
RESULTS · FINDING 1
Material identity is geometric, not magnitude
Chart: 
| Magnitude | Shape | Spatial | All features
Accuracy | 42.8 | 26.2 | 65.5 | 71
WHY
Spatial footprint features reach 65.5% vs 42.8% for raw magnitude — a ~1.5× gap.
Magnitude only says how hard you pressed; the shape of the contact says what it is.
6

## Slide 7
RESULTS · FINDING 2
Fusion beats either modality alone — the answer
Chart: 
| press | airhold | all
Deformation only | 67.5 | 68 | 62
Shear only | 65.5 | 62.5 | 55.5
Fused | 74.5 | 72.5 | 71
+4 to +9 pts
fusion over the best single modality, in every condition.
Compliant & textured materials (rubber, strawberry) activate the shear channel — confirming H1 & H3.
7

## Slide 8
RESULTS · FINDING 3
Temporal attention breaks the ceiling
Chart: 
| Classical SVM | Baseline CNN-LSTM | Attention (honest) | + Label smoothing
Honest accuracy (all, 10 materials) | 71 | 71 | 79.2 | 82.8
WHAT IT MEANS
Four classical/baseline models converge at ~71%. Temporal self-attention — re-weighting the loading sequence — lifts honest accuracy to ~80%.
A dual-branch variant added nothing → the gain is attention, not capacity.
8

## Slide 9
RESULTS · FINDING 4
Touch beats vision
Two PLA cubes — visually identical, different stiffness.
pla_hard
pla_soft
a camera cannot tell them apart
0
cross-confusions
In the honest confusion matrix the PLA pair is essentially never mistaken for one another.
The mechanical-response modality sees what vision physically cannot.
9

## Slide 10
RESULTS · ROBUSTNESS
Nine configurations: the gap is data-limited
Chart: 
| Label smooth | Combined | Weight decay | Augment-safe | Small model | +Translate | Crop window | Augment-aggr.
Honest test accuracy | 82.8 | 80.5 | 79.8 | 78.5 | 75.5 | 75.5 | 74.8 | 74
~80% ± 5–6%
honest reported band
Only gentle output regularization helps. Capacity cuts, cropping and augmentation are neutral or harmful — and the train–test gap stays ~+14% throughout. The binding limit is data quantity, not the model.
10

## Slide 11
DISCUSSION
Limitations & future work — stated honestly
Force confound
Hand collection leaves applied force entangled with identity — the dominant limit.
Small data
~20 trials/class → ±5–6% fold variance and a ~14% train–test gap.
Augmentation is narrow
Label lives in geometry+magnitude: rotation, scaling, even ±1px shift corrupt it.
Offline only
Single sensor/operator; no on-robot deployment result yet.
FUTURE WORK
Constant-force robotic collection
removes the confound that caps accuracy.
More trials per class
the one intervention that closes the gap.
On-robot deployment test
train-on-hand → deploy-on-Baxter transfer.
Richer 3D / contrastive pretraining
toward the FG-CLTP frontier.
11

## Slide 12
CONCLUSION
Fusing deformation and shear, and modeling the loading dynamics with attention, separates materials touch can distinguish but vision cannot.
+4–9 pts
fusion over single modality
~80% ±5–6%
honest, on 10 materials
0
PLA cross-confusions
The result is a complete, self-aware answer to the research question — bounded by data scale, not by method.
Amr Magdy Mohamed Elsayed Abdalla · S8082888 · / COGAR C2b